Basic setting for 2.0L TDI in A4

KNote:

To start the "Basic setting" function from Guided

Fault Finding:

1) Press mode button

2) Choose "Vehicle self-diagnosis" menu option

3) Choose "01-Engine electronics I" menu option

4) Select "04-Basic setting" and then the

number of the display group (e.g. 003 for exhaust gas recirculation)

003 Basic setting: Exhaust gas recirculation

1) Start engine

2) Start basic setting

3) Engine speed idling

4) To start the basic setting the

brake pedal and accelerator must be

pressed simultaneously!

KNote:

The exhaust gas recirculation is now switched

on and off intermittently.

Specifications with "EGR not active":

Engine speed: 1450 ... 1550 rpm

Position EGR

positioner    : -2 ... 2 %

Air mass: 400 ... 600 mg/stroke

Specificed position EGR

positioner    : -2 ... 2 %

Specifications with "EGR active":

Engine speed: 1450 ... 1550 rpm

Position EGR

positioner    : 30 ... 50 %

Air mass: 180 ... 390 mg/stroke

Specificed position EGR

positioner    : 30 ... 50 %

Record air mass values for TVH1 and TVH2 and

form difference. Difference must be at least 100 mg per stroke.

011 Basic setting: Turbocharger

1) Start engine

2) Start basic setting

3) Engine speed idling

4) To start the basic setting the

brake pedal and accelerator must be

pressed simultaneously!

KNote:

The turbocharger is now activated alternatingly at duty cycles

of -2 ... 2 % and 85 ... 95 %.

In this, the difference in the value 3 (actual charge pressure)

between CPC n.active and CPC active must be at least 80 mbar.

The engine speed is automatically increased.

035 Basic setting: Fuel supply pump

(not available in all vehicles)

1) Ignition ON

2) Start basic setting

KNote:

The electric fuel pump is then switched

ON/OFF intermittently. The noise of the pump may be perceptible

by touching the tank or may be quietly audible.

(IMPORTANT! There must be no open fuel supply lines!)

063 Basic setting: Adapting kickdown point

(only for vehicles with automatic gearbox)

1) Ignition ON

2) Start basic setting

3) Follow the instructions:

- First leave accelerator pedal in rest position (accelerator pedal)

- then press down accelerator pedal fully (press accelerator pedal)

4) Wait for status ADP.OK to be displayed, then

adaption is OK

5) Value is only stored in engine control unit after

approx. 5 seconds ignition OFF. (Ignition must not be

switched on again during this time!!!)