Display groups for 1.9l TDI in A4(BRB)

001 Injection quantity

Coolant temperature min. 75°C:

1) Engine speed

At idle: 860 ... 940 rpm

At full throttle: 2800 ... 3200 rpm

2) Injection quantity

At idle: 3.0 ... 90.0 mg/stroke

At full throttle: 40 ... 55 mg/stroke

3) Specified duration of delivery

At idle: 3 ... 9 °CA

At full throttle: 17 ... 26 °CA

4) Coolant temperature

Less than 75°C: => Warm up engine

002 Idling speed

Coolant temperature min. 75°C:

1) Engine speed

At idle: 860 ... 940 rpm

At full throttle: 2800 ... 3200 rpm

2) Accelerator pedal position

At idle: 0 %

At full throttle: 100 %

3) Operational status

X X X 1   AC ON1 X X X   Increased idling speed

4) Coolant temperature

Less than 75°C => Warm up engine

003 Exhaust gas recirculation

Coolant temperature min. 75°C:

1) Engine speed

At idle: 860 ... 940 rpm

At full throttle: 2800 ... 3200 rpm

2) Specified exhaust gas recirculation

At idle: 200 ... 300 mg/stroke

At full throttle: 750 ... 1200 mg/stroke

3) Actual exhaust gas recirculation

At idle: 180 ... 350 mg/stroke

At full throttle: 800 ... 1100 mg/stroke

4) EGR actuator activation

At idle: 20...90 %

At full throttle: 90...100 %

Exhaust gas recirculation shuts off after approx. 2 min

To activate: Press accelerator n > 1500 rpm

004 Solenoid valve pump nozzle control system

Coolant temperature min. 75°C:

1) Engine speed

At idle: 860 ... 940 rpm

At full throttle: 2800 ... 3200 rpm

2) Specified commencement of injection

At idle: 4 °b.TDC ... 2 ° aft.TDC

At full throttle: 13 ... 25 °b.TDC

3) Specified duration of delivery

At idle: 3 ... 9 °CA

At full throttle: 17 ... 26 °CA

4) Rotation angle

Idle/full throttle: -3 ... 3 °CA

005 Starting conditions

Stored from last engine start

1) Engine speed

860 ... 940 rpm

2) Starting injection quantity

7 ... 19 mg/stroke

3) Start synchronisation

000  Basic initialisation

001  Reset counter

002  Engine standstill or fault

003  Transitional states

004  Plausibility check phase

005  Plausibility check phase

006  Plausibility check phase

008  Plausibility check phase

016  Phase definition

028  Redundant start

032  Synchronisation phase

033  System positioning

048  Calculation sequences activated

064  System waiting for engine standstill

128  Dynamic plausibility check

4) Coolant temperature

[°C]

006 Switch settings

1) Current road speed

At least 40 - 80 km/h (at full throttle)

2) Pedal monitoring

X X X X X X X 1  Brake light switch pressed

X X X X X X 1 X  Brake pedal switch pressed(redundant)

X X X X X 1 X X  Clutch pedal switch pressed

X X X X 1 X X X  FGR enabled

X X X 1 X X X X  ACC enabled

X X 1 X X X X X  Main switch pressed

0 0 X X X X X X  ACC/CCS mode inactive

1 0 X X X X X X  State overspill

X 1 X X X X X X  ACC/CCS in control range

1 1 X X X X X X  ACC not enabled

3) Accelerator pedal position

[%]

4) CCS switch settings

X - X X X X X 1  Locked ON

X - X X X X 1 X  Touched OFF

X - X X X 1 X X  Touch-Down, reduce

X - X X 1 X X X  Touch-Up, increase

X - X 1 X X X X  Set

X - 1 X X X X X  Resume

1 - X X X X X X  Locked ON from hardware

007 Temperature senders

1) Fuel temperature

to 95 °C

2) Vacant

3) Intake air temperature (intake manifold temperature)

5 ... 80 °C

4) Coolant temperature

[°C]

008 Limiting torque 1

Coolant temperature min. 75°C:

1) Engine speed

At idle: 860 ... 940 rpm

At full throttle: 2800 ... 3200 rpm

2) Requested torque (accelerator pedal)

At idle: -5 ... 0 Nm

At full throttle: 270 ... 340 Nm

3) Torque limitation

At idle: 100 ... 200 Nm

At full throttle: 270 ... 320 Nm

4) Smoke limitation

At idle: 100 ... 200 Nm

At full throttle: >= Torque limitation (see zone 3)

010 Air quantities

Coolant temperature min. 75°C:

1) Intake air mass

At idle: 180 ... 350 mg/stroke

At full throttle: 800 ... 1100 mg/stroke

2) Ambient air pressure (altitude and weather dependent)

900 ... 1100 mbar

3) Actual charge pressure (altitude and weather dependent)

At idle: 900 ... 1150 mbar

At full throttle: 1850 ... 2400 mbar

4) Accelerator pedal position

At idle: 0 %

At full throttle: 100 %

Exhaust gas recirculation shuts off after approx. 2 min

To activate: Press accelerator n > 1500 rpm

011 Charge pressure control

Coolant temperature min. 75°C:

1) Engine speed

At idle: 860 ... 940 rpm

At full throttle: 2800 ... 3200 rpm

2) Specified charge pressure

At idle: 900 ... 1150 mbar

At full throttle: 1900 ... 2200 mbar

3) Actual charge pressure (altitude and weather dependent)

At idle: 900 ... 1150 mbar

At full throttle: 1850 ... 2300 mbar

4) Charge pressure limitation duty cycle

At idle: 40...90 %

At full throttle: 20...80 %

012 Preheating system

1) Glow status

0 0 0 0 0 0 0 0  Waiting for coolant temperature

0 0 0 0 0 0 0 1  Waiting for ECO start request

0 0 0 1 0 0 0 0  Glow period

0 1 0 1 0 0 0 0  No glow

1 0 1 1 0 0 0 0  After-glow

1 1 0 0 0 0 0 0  No start glow

1 1 1 1 0 0 0 0  Intermediate glow

0 0 1 1 0 0 0 0  Readiness glow

0 1 1 1 0 0 0 0  Start glow

1 0 1 1 0 0 0 1  Waiting for after-glow

1 1 0 1 0 0 0 0  No after-glow

1 1 1 1 0 0 0 1  Waiting for intermediate glow

1 1 1 1 1 1 1 1  No glow

2) Glow period

[s]

3)Vehicle voltage

13 ... 15 V

4) Coolant temperature

[°C]

013 Smooth running control

Measured values at idle, coolant temperature min. 75°C:

1) Cylinder 1 injection quantity variation

2) Cylinder 2 injection quantity variation

3) Cylinder 3 injection quantity variation

4) Cylinder 4 injection quantity variation

Permissible values, cylinders 1 to 4: -2.8 ... 2.8 mg/stroke

015 Fuel consumption

Coolant temperature min. 75°C:

1) Engine speed

At idle: 860 ... 940 rpm

2) Engine torque

At idle: 25 ... 60 Nm

3) Fuel consumption

[ltr/h]

4) Required injection quantity (accelerator pedal)

At idle: -5 ... 0 Nm

016 Additional heater

1) Alternator load

5...95 %

2) Shut-off conditions

Additional heater shut off because:

x x x x x x x 1   Coolant > 80°C

x x x x x x 1 x   Alternator fault

x x x x x 1 x x   Battery voltage too low

x x x x 1 x x x   Engine speed too low

x x x 1 x x x x   Start delay active

x x 1 x x x x x   Coolant temperature sender or

intake air temperature sender G42 defective or output stage

additional heater defective

1 x x x x x x x   Ambient temperature above 5°C

3) Activation of heater elements

x 1   PTC stage 1(low heat output relay J359) on

1 x   PTC stage 2(high heat output relay J360) on

4)Vehicle voltage

13 ... 15 V

017 Readiness code (EOBD)

1) CARB mode 01 DATA A

X - - - 0 0 0 0  No fault messages stored

0 - - - X X X X  MIL lamp OFF

1 - - - X X X X  MIL lamp ON

2) CARB mode 01 DATA B

- X X X - X X 1  Activation misfire detection (1 = present)

- X X X - X 1 X  Activation fuel system (1 = present)

- X X X - 1 X X  Activation complete system (1 = present)

- X X 0 - X X X  EOBD test misfire detection completed *)

- X 0 X - X X X  EOBD test fuel system completed

- 0 X X - X X X  EOBD test overall system completed

3) CARB mode 01 DATA C

X X 1 - - - - -  Activation lambda probe (1 = present)

X 1 X - - - - -  Activation lambda probe heating (1 = present)

1 X X - - - - -  Activation EGR (1 = present)

4) CARB mode 01 DATA D

X X 0 - - - - -  EOBD test lambda probe completed *)

X 0 X - - - - -  EOBD test lambda probe heating completed *)

0 X X - - - - -  EOBD test EGR completed

*) Depending on equipment spec

018 Solenoid valves status

1) Cylinder 1

2) Cylinder 2

3) Cylinder 3

4) Cylinder 4

Key - cylinders 1 to 4:

000  Fault-free control

002  Closed-loop control at start

004  Small injection quantity or solenoid valve off

008  Maximum current reached

016  BIP outside control window

032  Number of scans too low

064  Conversion error

128  No BIP evaluation possible

023 Solenoid valve switching times

1) Cylinder 1

2) Cylinder 2

3) Cylinder 3

4) Cylinder 4

Values, cylinders 1 to 4: -100 ... 100 s

028 Pedal sender

1) Accelerator pedal sender 1

Accelerator pos.: 0 %   A  0.25 ... 0.35 V

100 %   A  4.10 ... 4.70 V

2) Accelerator pedal sender 2

No data

3) Operational status

X X X 1   AC ON

X X 0 X   Idling speed switch ON

X 1 X X  Kickdown switch ON (automatic gearbox only)

1 X X X   Increased idling speed

4) Accelerator pedal position

0...100 %

051 Speed recording

1) Engine speed

[rpm]

2) Camshaft speed

Engine speed/2  rpm  +-50

3) Start synchronisation

000  Basic initialisation

001  Reset counter

002  Engine standstill or fault

003  Transitional states

004  Plausibility check phase

005  Plausibility check phase

006  Plausibility check phase

008  Plausibility check phase

016  Phase definition

028  Redundant start

032  Synchronisation phase

033  System positioning

048  Calculation sequences activated

064  System waiting for engine standstill

128  Dynamic plausibility check

4) Injection sequence shut-off status

No data

062 Engine cooling 3

1) Coolant temperature

[°C]

2) Vacant

3) Ambient temperature

-20 ... 50 °C

4) Intake air temperature (intake manifold temperature)

5 ... 80 °C

063 Engine cooling 4

1) AC compressor refrigerant pressure

AC OFF: 0 ... 8 bar

AC ON: 5 ... 30 bar

2) AC compressor load torque

AC OFF: 0 Nm

AC ON: 2 ... 10 Nm

3) Vacant

4) AC compressor shut-off status

001  Vehicle starting off

002  OFF because starting off

004  Vehicle accelerating

008  OFF because accelerating

016  Shut-off because starting

032  System fault detected

064  Shut-off because of system fault

128  OFF because of idling speed undercut

064 Engine cooling 5

1) Coolant temperature

[°C]

2) Vacant

3) Fan 1 duty cycle

Radiator fan OFF: 8...9 %

Radiator fan ON: 12...100 %

4) Vacant

067 Particulate filter exhaust gas values 1

Condition: v=const 50-60km/h,3rd gear, n<=3000 rpm

A Values valid only during regeneration

1) Temperature upstream of turbocharger

> 690°C        (after 10 seconds)

2) Temperature before particulate filter

> 150°C

3) Pressure difference over particulate filter

No data

4) Offset differential pressure in overrun

No data

068 Particulate filter exhaust gas values 2

Condition: v=const 50-60km/h,3rd gear, n<=3000 rpm

A Values valid only during regeneration

1) Charge coefficient

< 50%           (at 50% regeneration starts)

2) Ash mass

<60 g *)

3) Ash learned value

No data

4) Vacant

*) After replacing filter set axle mass with VAG tester to 0

069 Particulate filter regeneration status 1

Condition: v=const 50-60km/h,3rd gear, n<=3000 rpm

A Values valid only during regeneration

1) Regeneration status 1

0XXX XXXX   Interruption of regeneration by overrun, high

torque request or fast speed

requirement

2) Regeneration status 2

No data

3) Regeneration status 3

No data

4) Regeneration status 4

XXXX XXX1   Corresponds to regeneration stage 1

XXXX XX1X   Corresponds to regeneration stage 2

070 Particulate filter regeneration status 2

Condition: v=const 50-60km/h,3rd gear, n<=3000 rpm

A Values valid only during regeneration

1) Regeneration status 4

XXXX XXX1   Corresponds to regeneration stage 1

XXXX XX1X   Corresponds to regeneration stage 2

2) Elapsed lockout time

[s]

3) Regeneration counter

No data

4) Status of successful regenerations

0...8

9     Regeneration disabled

073 Particulate filter vehicle data

Condition: v=const 50-60km/h,3rd gear, n<=3000 rpm

A Values valid only during regeneration

1) Fuel consumption since last regeneration

No specifications

2) Distance since last regeneration

No specifications

3) Time since last regeneration

No specifications

4) Vacant

074 Particulate filter exhaust gas values 3

Condition: v=const 50-60km/h,3rd gear, n<=3000 rpm

A Values valid only during regeneration

1) Engine speed

[rpm]

2) Temperature upstream of turbocharger

> 690°C

3) Lambda value

1,0-2,0

4) Vacant

075 Particulate filter emission values 4

A Values valid only during regeneration

1) Temperature upstream of turbocharger

> 690°C

2) Temperature before particulate filter

> 150°C

3) Charge coefficient

< 50% (as from 50% regeneration starts when driving)

4) Temperature after particulate filter

> 50°C

090 EOBD exhaust gas recirculation 1

Condition: Engine idling,v=0km/h,no gear engaged.

Handbrake on; set engine speed with accelerator pedal

If MVB 90/4 bit 1 is set to 1, read MVB 91

1) Engine speed

760...940         EGR test not active

1200...2000       EGR test active

2) Injection quantity

3 ... 9 mg/stroke EGR test not active

No data     EGR test active

3) Specified exhaust gas recirculation

200 ... 300 mg/stroke   EGR test not active

No data     EGR test active

4) Status EGR control deviation

0000 0000         EGR test not active

0000 0001         EGR test active

091 EOBD exhaust gas recirculation 2

Condition: Engine idling,v=0km/h,no gear engaged.

Handbrake applied

1) EGR actuator permissible positive control deviation

0...324

2) EGR actuator permissible negative control deviation

-324...0

3) Air mass specification

As MVB 90/3

4) Control deviation

Value must be within pos./neg. control deviation range

(MVB 91/1/2)

125 CAN bus communication 1

1) Gearbox control unit

2) ABS control unit

3) Dash panel insert control unit

4) Airbag control unit

Each 1 bit: 0 = inactive

1 = active

--- = not fitted

126 CAN bus communication 2

1) Air conditioner control unit

2) Vacant

3) Onboard power supply control unit

4) ACC control unit

Each 1 bit: 0 = inactive

1 = active

--- = not fitted

127 CAN bus communication 3

1) Four-wheel drive control unit

2) Adaptive suspension control unit

3) Vacant

4) Steering column module control unit

Each 1 bit: 0 = inactive

1 = active

--- = not fitted

128 CAN bus communication 4

1) Gateway control unit

2) Battery energy management control unit

3) Vacant

4) Vacant

Each 1 bit: 0 = inactive

1 = active

--- = not fitted