Display groups for A2 (ANY)

001 Injection quantity

Measured values at idle, coolant temperature min. 80°C:

1) Engine speed

800..0.880 rpm

2) Injection quantity

3.0...8.0 mg/stroke   A OK

Below 3.0 mg/stroke  A Check pump/nozzle units

Above 8.0 mg/stroke A Engine too cold

Fuel shortage

Air in fuel system

Check pump/nozzle units

3) Specified duration of delivery

3...7 °CA    A OK

4) Coolant temperature

80...110 °C   A OK

Less than 80 °C A Warm up engine

002 Idling speed

Measured values at idle, coolant temperature min. 80°C:

1) Engine speed

800..0.880 rpm A OK

2) Accelerator pedal position

0.0 %        A OK

Above 0,0 % A Accelerator pedal sender incorrectly

set or defective

Open circuit in wiring

3) Operational status

X  X  1:    AC compressor on (if air conditioner fitted)

X  1  X:    Idling speed switch closed

1 X X :     Idling speed increased because air conditioner on

(if air conditioner fitted)

0 1 0 :     Specification

4) Coolant temperature

80...110 °C   A OK

Less than 80°C A Warm up engine

003 Exhaust gas recirculation

Measured values at idle, coolant temperature min. 85°C:

1) Engine speed

800..0.880 rpm A OK

2) Intake air mass (specified)

200..0.270 mg/stroke A OK

Above 270 mg/stroke A Engine too cold A Warm up

3) Intake air mass (actual)

As specified air mass in display zone 2 (tolerance +-20 mg/stroke) AOK

Insufficient air mass: Unmetered air in intake

Excessive exhaust gas recirculation => Check

Excessive air mass:  Engine too cold A warm up

Insufficient exhaust gas recirculation => Check

Engine running for 10 min. at idle => Briefly

press accelerator

Constant readout: Substitute value

4) EGR valve duty cycle

30...80 %

004 Activation of pump/nozzle valves

Measured values at idle, coolant temperature min. 80°C:

1) Engine speed

800..0.880 rpm

2) Specified commencement of injection

0...3° bef.TDC A OK

Below 3°b.TDC  A Engine too cold A warm up

3) Specified duration of delivery

4..0.6 °CA    A OK

4) Synchronisation angle

-3...+3°CA A OK

Measured values at full throttle (test drive in 3rd or 4th gear),

Coolant temperature min. 80°C:

1) Engine speed

2800..0.3200 rpm

2) Specified commencement of injection

16...22 °bef.TDC A OK

3) Specified duration of delivery

15..0.23 °CA    A OK

4) Synchronisation angle

[°CA]

005 Starting conditions

1) Engine speed

[rpm]

2) Starting injection quantity

[mg/stroke]

Stored from last engine start

3) Start synchronisation

[]

4) Coolant temperature

[°C]

006 Switch settings

1) Vehicle speed

[km/h]

2)Switch settings

X X 1   Brake light switch F closed

X 1 X   Brake pedal switch F47 open

1 X X   Clutch pedal switch F36 open (in vehicles with

automatic gearbox readout always 1)

3) Accelerator pedal position

[%]

4) Cruise control system

0   = Vehicles with CCS, CCS off

1   = Vehicles with CCS, CCS on

255 = Vehicles without cruise control

007 Temperatures

Measured values at ignition on, engine off, cooled:

1) Fuel temperature

[°C]

at fuel temperature sender G81

2) Fuel cooling status

0% A Off

3) Intake manifold temperature

[°C]

at intake manifold temperature sender G72

4) Coolant temperature

[°C]

at coolant temperature sender G62

008 Limit quantities

Measured values at full throttle (test drive in 3rd or 4th gear),

coolant temperature not below 80°C):

1) Engine speed

2800..0.3200 rpm

2) Injection quantity (driver input)

45..0.51 mg/stroke A OK

Below 45 mg/stroke  A No full throttle or accelerator pedal sender

defective

3) Injection quantity limitation via engine speed (torque limitation)

31..0.36 mg/stroke

Below 31 mg/stroke A Speed too high or too low

4) Injection quantity limitation based on intake air mass

29..0.40 mg/stroke

Below 29 mg/stroke A Intake air mass too low,

EGR quantity too high

009 Injection quantity limitation

1) Engine speed

[rpm]

2) Injection quantity (cruise control active)

[mg/stroke]

3) No readout

4) Limit quantity

[mg/stroke]

010 Air quantities

Measured values at full throttle (test drive in 3rd or 4th gear),

coolant temperature not below 80°C):

1) Intake air mass

Above 600 mg/stroke A OK

Less than 600 mg/stroke   A Engine speed below 2000 rpm or

above 4000 rpm)

Charge pressure too low A Observe display zone 3, unmetered air

between air mass meter and turbocharger,

air mass meter possibly defective

2) Ambient air pressure

[mbar]

3) Intake manifold pressure (charge pressure)

1650...2140 rpm A OK

Outside tolerance   A Charge pressure control defective => Display group 11

4) Accelerator pedal position

Press down accelerator pedal: 100%

Less than 100 A Accelerator pedal not pressed down, accelerator pedal

sender G79 incorrectly set or defective

011 Charge pressure control

1) Engine speed

800..0.880 rpm

2) Specified charge pressure

900..0.1100 mbar

3) Actual charge pressure

As specified charge pressure in display zone 2

4) Duty cycle, charge pressure control solenoid valve

25...95 %

011 Charge pressure control

Measured values at full throttle (test drive in 3rd or 4th gear),

coolant temperature not below 80°C):

1) Engine speed

2800..0.3200 rpm

2) Specified charge pressure

1650...2100 mbar

3) Actual charge pressure

As specified charge pressure in display zone 2 (tolerance +-40 mbar):OK

Inadequate charge pressure  A No charge pressure control, turbocharger defective

Excessive charge pressure   A Solenoid valve -N75 sticking, charge pressure control tube detached or clogged,

linkage on turbocharger rusted up, vacuum unit

defective

4) Duty cycle, charge pressure control solenoid valve

[%]

012 Preheating system

1) Glow status

[]

2) Glow period

[s]

3) Vehicle voltage

[V]

4) Coolant temperature

[°C]

013 Smooth running control

Measured values at idle

1) Cylinder 1 injection quantity variation:

[mg/stroke]

2) Cylinder 2 injection quantity variation:

[mg/stroke]

2) Cylinder 3 injection quantity variation:

[mg/stroke]

4) No readout

I Permissible tolerance: -1.9...+1.9 mg/stroke

I If one or more cylinders outside tolerance:

A Check pump/nozzle units.

015 Fuel consumption

1) Engine speed

[rpm]

2) Actual injection quantity

[mg/stroke]

3) Fuel consumption

[ltr/h]

4) Injection quantity request

[mg/stroke]

Driver input via accelerator pedal

016 Additional electric heater PTC

1) Alternator load

[%]

5...95%  A Additional electric heater (PTC) can be activated

5...100% A Fuel-powered additional heater can be activated

2) Additional heater

Additional heater shut offs because:

x x x x x x x 1   Coolant > 80°C or intake manifold temperature > +5°C

x x x x x x 1 x   Alternator defective

x x x x x 1 x x   Battery voltage < 9 V

x x x x 1 x x x   Engine speed < 400 rpm

x x x 1 x x x x   Engine start within last 10 seconds

x x 1 x x x x x   Coolant temperature sender or

intake manifold temperature sender G72 defective or power stage of

additional heater defective

x 1 x x x x x x   No request to engine control unit (e.g. OFF

or ECON button pressed)

1 x x x x x x x   Ambient temperature above 5°C

3) Activation of heater elements

To model year 2002 (900 Watt PTC heater)

x 1   Low heating output relay J359 on

1 x   High heating output relay J360 on

From model year 2003 phase-in (1500 Watt PTC heater)

x 1   Low heating output relay J359 on

In vehicles with 1.2l TDI engine with emissions standard D4(3l Eco for

Germany) no additional heater is currently specified.

4) Supply voltage

13.5...14.8 V

Engine control unit

018 Pump/nozzle valve status

1) Pump/nozzle valve cylinder 1

x x

2) Pump/nozzle valve cylinder 2

x x

3) Pump/nozzle valve cylinder 3

x x

4) No readout

If display zone 1, 2 or 3 shows a numbe instead of a 0

the following faults causes may apply:

I Pump/nozzle valve defective A check

I Open circuit

I  Lack of fuel

I Air in fuel