Basic setting for 2.0l 4V TDI in A6

KNote:

To start the "Basic setting" function from Guided

Fault Finding:

1) Press mode button

2) Choose "Vehicle self-diagnosis" menu option

3) Choose "01-Engine electronics I" menu option

4) Select "04-Basic setting" and then the

number of the display group (e.g. 003 for exhaust gas recirculation)

All values given relate to measurements on the warmed-up

engine (coolant temperature >75°C) and at sea level. All consumers

should be switched off prior to measuring.

003 Basic setting: Exhaust gas recirculation

1) Start engine

2) Start basic setting

3) Engine speed idling

KNote:

The exhaust gas recirculation is now switched

on and off intermittently.

The difference from ARF_actual between EGR active (0..10%)

and EGR n.active (20..40%) must be at least 100 mg per stroke

011 Basic setting: Turbochargers

1) Start engine

2) Start basic setting

3) Engine speed idling

KNote:

The turbocharger is now activated alternatingly at duty cycles

of 0 ... 10% (OFF) and 90 ... 100% (ON).

In this, the difference in the value 3 (actual charge pressure)

between CPC n.active and CPC active must be at least 80 mbar.

The engine speed is automatically increased.

- As a function test for the charge pressure control an

acceleration test at full throttle is additionally required (3000 rpm,

100% accelerator position, 2nd gear, measured value block 11)

035 Basic setting: Fuel supply pump

1) Start basic setting

KNote:

The electric fuel pump is then switched

ON/OFF intermittently. The noise of the pump may be perceptible

by touching the tank or may be quietly audible.

(IMPORTANT! There must be no open fuel supply lines!)

050 Basic setting: Compression test

KNote:

Application of this basic setting is only described in Guided

Fault Finding, as in this compression test

different algorithms are necessary for analysis.

063 Basic setting: Adapting kickdown point

(only for vehicles with automatic gearbox)

1) Ignition on

2) Start basic setting

3) Follow the instructions:

- First leave accelerator pedal in rest position (accelerator pedal)

- then press down accelerator pedal fully (press accelerator pedal)

4) Wait for status ADP.OK to be displayed, then

adaption is OK

5) Value is only stored in engine control unit after

approx. 5 seconds ignition OFF. (Ignition must not be

switched on again during this time!!!)