003 Basic setting: Exhaust gas recirculation

1) Coolant temperature at least 80 °C

2) Switch off ignition briefly, then start engine

3) Start basic setting

4) First press brake pedal, then accelerator pedal

Both pedals must be pressed during basic setting.

If they are not, the basic setting is aborted.

5) Wait for the engine speed rise to approx. 1000 rpm

KNote:

The exhaust gas recirculation is now switched

on and off intermittently.

Specifications with "EGR not active":

Engine speed:     approx. 1000 rpm

Activation:       EGR not active

Air mass bank 1:  370 ... 630 mg/stroke

Air mass bank 2:  370 ... 630 mg/stroke

Specifications with "EGR active":

Engine speed:     approx. 1000 rpm

Activation:       EGR active

Air mass bank 1:   90 ... 210 mg/stroke

Air mass bank 2:  120 ... 260 mg/stroke

033 Basic setting: Turbocharger

1) Coolant temperature at least 80 °C

2) Switch off ignition briefly, then start engine

3) Start basic setting

4) First press brake pedal, then accelerator pedal

Both pedals must be pressed during basic setting.

If they are not, the basic setting is aborted.

5) Wait for the engine speed rise to approx. 1450 rpm

KNote:

The turbochargers are now activated alternatingly at duty cycles

of 40 % and 100 %, so that in one

time interval the right side turbocharger is activated at 100 % and

at the same time the left is activated at 40 %, and in the next

interval the turbocharger duty cycles  are swapped.

Specifications with "Turbocharger 1 on":

Engine speed:     approx. 1450 rpm

Activation:       Turbocharger 1 on

Air mass bank 1:  690 ... 910   mg/stroke

Air mass bank 2:  100 ... 250 mg/stroke

Specifications with "Turbocharger 2 on":

Engine speed:     approx. 1450 rpm

Activation:       Turbocharger 2 on

Air mass bank 1:   80 ... 220 mg/stroke

Air mass bank 2:  720 ... 940 mg/stroke

040 Basic setting: Intake manifold flaps

1) Coolant temperature at least 80 °C

2) Switch off ignition briefly, then start engine

3) Start basic setting

4) First press brake pedal, then accelerator pedal

Both pedals must be pressed during basic setting.

If they are not, the basic setting is aborted.

5) Wait for the engine speed rise to approx. 2800 rpm

KNote:

The intake manifold flaps are now activated alternatingly at duty cycles

of 20 % and 80 %, so that in one

time interval the right side intake manifold flap is activated at 80 % and

at the same time the left is activated at 20 %, and in the next

interval the intake manifold flap duty cycles  are swapped.

Specifications with "flap open":

Engine speed:     approx. 2800 rpm

Activation:       Flap open

Air mass bank 1:  570 ... 1030 mg/stroke

Air mass bank 2:  570 ... 1030 mg/stroke

Specifications with "flap closed":

Engine speed:     approx. 2800 rpm

Activation:       Flap closed

Air mass bank 1:  570 ... 1030 mg/stroke

Air mass bank 2:  570 ... 1030 mg/stroke

063 Adapting kickdown point

1) Switch off ignition briefly, then ignition on

2) Start basic setting

3) Press down accelerator pedal until status ADP OK is displayed

4) Value is only stored in engine control unit after

approx. 10 seconds ignition OFF.

Specifications:

Sender 1 Accelerator position:  X ... X %

Sender 2 Accelerator position:  X ... X %

---

Status:    ADP.OK